Panzer II Ausf. J (VK1601)

Classification: Light Tank 
Manufacturer: MAN 
Start of Produciton: April 1942 
End of Produciton: December 1942 
Prod. Quantity: 22 
Crewstrength: 3 
Length: 4,81 m 
Width: 2,28 m 
Height: 2,15 m 
Engine: Maybach HL45 
Power: 112 kW 
Type of Fuel: Gasoline 
Fuel Consumption: n.a. 
Weight: 18,00 t 
Power/Weight ratio: 6,22 kw/t 
Ground Pressure: n.a. 
max. Speed onroad: 32 km/h 
max. Speed offroad: n.a. 
max. Range onroad: n.a. 
Suspensiontype: Torsion Bar 
Turning Radius: 4,80 m 
Armoring as following: 
Turret Front: 113 mm 
Turret Sides: 54 mm 
Turret Rear: 54 mm 
Hull Front upper: 81 mm 
Hull Front lower: 85 mm 
Hull Sides upper: 50 mm 
Hull Sides lower: 50 mm 
Hull Rear upper: 50 mm 
Hull Rear lower: 50 mm 
Turret Top: 25 mm 
Hull Top: 25 mm 
Hull Bottom: 25 mm 
Armament & Ammo as following: 
1x 20mm KwK38 L/55 in Turret w. 180 Rounds 
1x 7,92mm MG34 coaxial w. 2700 Rounds 
Turret Traverse Rate: 
11 sec @ 360°

Some sources state that they were armed with a 14.5mm AT Rifle (Cant remember the name) instead of the 20mm Cannon. Of the 22 made half were sent to the Balkans while the other half went to France. All those sent to France were destroyed in during the Normandy fighting, while the last few in the Balkans simply vanish from all records in the last few months of the war. The Tank was meant as a Infantry Support tank.